## Slide 2
Film/Sensor
Where the light is recorded
Lens
Bends the light
Trajectory of light
Subject
Source of light
Focusing
A look at the overall camera system

## Slide 3
Light converges at sensor
Light converges past sensor
Light converges before sensor
Result:
‘In focus’
‘Out of focus’
‘Out of focus’

## Slide 4
Result:
‘In focus’
Circle of confusion
Image doesn’t have to perfectly converge. If it converges within a “circle of confusion”, it is still ‘in focus’
‘In focus’
‘Out of focus’

## Slide 5
In focus
Out of focus
Out of focus

## Slide 6
Things at a certain distance are “in focus” (perfectly sharp)
The further from this distance, the blurrier things are
There is a range of distance where things are ‘sharp enough’ to be considered ‘in focus’. This range is known as the “depth of field”
Amount of Blur
Depth of field

## Slide 7
Depth of field
Range that is ‘in focus’
Focus point
Near limit of focus
Far limit of focus
Film/Sensor
Where the light is recorded
Circle of confusion
Maximum non-convergance allowed to be ‘in focus’

## Slide 8
Depth of field
Circle of confusion
When using a bigger lens (larger aperture), the depth of field shrinks

## Slide 9
Depth of field
Circle of confusion
Longer subject distances mean larger depth of field range

## Slide 10
Circle of confusion
Longer focal lengths mean smaller depth of field range
Depth of field

## Slide 11
A = aperture f-number (e.g. f5.6)
f = focal length (e.g. 50mm)
d = distance to subject (e.g. 3000mm)
c = circle of confusion (e.g. .02mm)
Factors to note:
Smaller apertures (larger f-number) gives larger depth of field
Shorter focal length gives larger depth of field
Longer distance to subject gives larger depth of field
Larger circle of confusion gives larger depth of field

## Slide 12
Uses of large depth of field
Landscape/scenery
Architecture
Small depth of field
Macro

## Slide 13
Uses of small depth of field
Portraits
Flowers
Sports
Isolation