## Slide 1
Digital Photography DeCal
EECS98/198
Nathan Yan
About this course
-Technology of Camera Systems
-Photographic Technique
-Digital Lightroom
About Me
^-doesn’t know anything about what he’s talking about
About You
In case you were wondering, this is the noise signature of an image, inverted

## Slide 2
All cameras, film or digital, work the same:
Photons are projected onto a photo-sensitive plane which records the light information
How it works

## Slide 3
How it works
By confining light to only photons which pass through a certain point, we begin to resolve “detail”
Image processor

## Slide 4
History of Camera Development
Many pinhole-type cameras dating back to the 11th century
Joseph Niépce recorded the first photograph in 1826, using a photo-sensitive silver/chalk mixture
Development of recording mediums more responsive to light: wet plates, dry plates
George Eastman introduces photographic film in 1885, and debuts the “Kodak” camera in 1888 – a cheap and easy to operate camera that began to popularize cameras
Oskar Barnack developed the Leica camera in 1925, which popularized 35mm film standard
Ihagee introduced the first single-lens reflex camera, Exakta, in 1933, allowing photographers to view image “through the lens”
Auto-focus developed in the Konica C35AF in 1977

## Slide 5
History of Digital Camera Development
Began with charged couple device (CCD) cameras that recorded to analog media
  Steve Sasson produced the first for Kodak in 1973
    Solid state CCD that recorded output onto cassette tape
    Resolution: 10,000 pixels, or 0.01 megapixels
First practical use in 1984, for journalism
  Canon RC-701 recorded images onto “video floppies”
  During 1984 Olympics images could be transmitted via telephone lines, and image quality was acceptable for newsprint
JPEG image compression standard introduced in 1988
First true digital camera: Fuji DS-1P debuted in 1988, recording a computerized image file to onboard memory
First camera with live image feed to LCD: Casio QV-10 in 1995
First “professional” digital SLR camera natively designed: 2.74MP Nikon D1 in 1999
First affordable “consumer” digital SLR: 6MP Canon Digital Rebel 300D in 2003 - $1000

## Slide 6
Input:
Light «photons»
Output:
Electrical signals
The Imaging Sensor

## Slide 7
Si
Si
Si
Si
Si

## Slide 8
Bucketloads of Electrons!
Many electrons
Voltage: High
Implication: Many photons detected, bright exposure
Result: bright image
Few electrons
Voltage: Low
Implication: Few photons detected, dark exposure
Result: dark image
Max electrons
Voltage: Max
Implication: Max photons detected, brightest exposure
Result: White image
No electrons
Voltage: Zero
Implication: No photons detected, darkest exposure
Result: Black image

## Slide 9
Si
Si
Si
101010100100
Image processor
Photons
Photoelectrons
Electrical signal
Accumulated charge
Digital representation of electrical signal
Image file
Amplifier
Analog-to-Digital Converter
Amplified electrical signal
Photons
Electrons
Voltage Reading
Voltage Signal
Image Brightness
Shutter speed
Aperture
Quantum efficiency
Signal Amplification
Digital Multiplication

## Slide 10
Photo wells
Sensors
?
?
?
We know the pixel is bright, but what color is it?
Problem: Since the sensor only records light intensity, we can’t differentiate between colors! Thus, imaging sensors only record in black and white
Solution: Color filtering, the most common form being the Bayer filter

## Slide 11
BAYER FILTER
Designates individual photosites to be either red, green, or blue (RGB)
Respective color filters are placed over each photosite
Thus, only the light energy corresponding to that color’s wavelength reaches the sensor
Thus the sensor can interpret the energy recorded at that photosite to be a measure of that certain color
Knowing the intensities of red, green, and blue light, we can derive the actual color

## Slide 12
BAYER FILTER
Color offset
Since each photosite must be designated some color, the Bayer pattern of blue, green, and red photosites if offset, with blue tending towards top-left and red tending towards bottom-right
Loses 2/3 of light information
At each photosite, 2 of 3 colors are filtered out, and light information discarded
  Workarounds:
  -Expose pictures for 3x time
  -not practical for photography
  -Demosiac algorithms to interpolate missing 2/3 data
Drawbacks of…
Actual Image
Raw Bayer Output
Demosiaced Bayer Output

## Slide 13
Photon
rate
Time
End of exposure
End of exposure
Ideal
Rate of incoming light is constant
Real life
Rate of incoming light is fluctuating
Photon
rate
Time
How much fluctuation?
√n
Dictated by Poisson (pwasõ) Distribution
For n total photons in exposure,
standard deviation =

## Slide 14
Photons collected = n + √n
If n = 10,000 photons,
Photons collected = 10,000 + √10,000 = 10,000 + 100 photons
10,000 photons
9,900
photons
10,100
photons
9,950
photons
√n, so what?
Variable brightness = noise!
Noise monster One of the photographer’s worst enemies

## Slide 15
Chart: Proportion of fluctuation
| 100 | 120 | 150 | 200 | 300 | 400 | 500 | 700 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 9999
sqrt(n)/n | 0.1 | 0.091287 | 0.08165 | 0.070711 | 0.057735 | 0.05 | 0.044721 | 0.037796 | 0.031623 | 0.02582 | 0.022361 | 0.02 | 0.018257 | 0.016903 | 0.015811 | 0.014142 | 0.01291 | 0.011952 | 0.01118 | 0.010541 | 0.010001
Proportion of Photon Fluctuation (√(n)/n)
Photons

## Slide 16
Chart: 
| 80000 | 40000 | 20000 | 10000 | 5000
Canon 5D | 0.0035355 | 0.005 | 0.0070711 | 0.01 | 0.014142
Nikon D300 | 0.0084515 | 0.011952 | 0.016903 | 0.023905 | 0.033806
Sony H9 | 0.01857 | 0.026261 | 0.037139 | 0.052523 | 0.074278 | 0.10505
Proportion of Photon Fluctuation (√(n)/n)
Photons

## Slide 17
Chart: 
| 80000 | 40000 | 20000 | 10000 | 5000
Canon 5D | 0.0035355 | 0.005 | 0.0070711 | 0.01 | 0.014142
Nikon D300 | 0.0084515 | 0.011952 | 0.016903 | 0.023905 | 0.033806
Sony H9 | 0.01857 | 0.026261 | 0.037139 | 0.052523 | 0.074278 | 0.10505
Proportion of Photon Fluctuation (√(n)/n)
Photons

## Slide 18
x001
x010
x001
x100
x110
x111
x101
x110
x000
x000
x010
x101
x010
x011
x110
x110