## Slide 1
Photon
rate
Time
End of exposure
End of exposure
Ideal
Rate of incoming light is constant
Real life
Rate of incoming light is fluctuating
Photon
rate
Time
How much fluctuation?
√n
Dictated by Poisson (pwasõ) Distribution
For n total photons in exposure,
standard deviation =

## Slide 2
Photons collected = n + √n
If n = 10,000 photons,
Photons collected = 10,000 + √10,000 = 10,000 + 100 photons
10,000 photons
9,900
photons
10,100
photons
9,950
photons
√n, so what?
Variable brightness = noise!
Noise monster One of the photographer’s worst enemies

## Slide 3
Chart: Proportion of fluctuation
| 100 | 120 | 150 | 200 | 300 | 400 | 500 | 700 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 9999
sqrt(n)/n | 0.1 | 0.091287 | 0.08165 | 0.070711 | 0.057735 | 0.05 | 0.044721 | 0.037796 | 0.031623 | 0.02582 | 0.022361 | 0.02 | 0.018257 | 0.016903 | 0.015811 | 0.014142 | 0.01291 | 0.011952 | 0.01118 | 0.010541 | 0.010001
Proportion of Photon Fluctuation (√(n)/n)
Photons

## Slide 4
Chart: 
| 80000 | 40000 | 20000 | 10000 | 5000
Canon 5D | 0.0035355 | 0.005 | 0.0070711 | 0.01 | 0.014142
Nikon D300 | 0.0084515 | 0.011952 | 0.016903 | 0.023905 | 0.033806
Sony H9 | 0.01857 | 0.026261 | 0.037139 | 0.052523 | 0.074278 | 0.10505
Proportion of Photon Fluctuation (√(n)/n)
Photons

## Slide 5
Chart: 
| 80000 | 40000 | 20000 | 10000 | 5000
Canon 5D | 0.0035355 | 0.005 | 0.0070711 | 0.01 | 0.014142
Nikon D300 | 0.0084515 | 0.011952 | 0.016903 | 0.023905 | 0.033806
Sony H9 | 0.01857 | 0.026261 | 0.037139 | 0.052523 | 0.074278 | 0.10505
Proportion of Photon Fluctuation (√(n)/n)
Photons

## Slide 6
Chart: 
| 2900 | 1450 | 725 | 362.5 | 181.25 | 90.624999999999986
Sony H9 | 0.01857 | 0.026261 | 0.037139 | 0.052523 | 0.074278 | 0.10505
Proportion of Photon Fluctuation (√(n)/n)
Photons

## Slide 7
Chart: 
| 3308.4507042253372 | 1654.2253521126686 | 827.11267605633429 | 413.55633802816703 | 206.77816901408357
Canon A570IS | 0.017386 | 0.024587 | 0.034771 | 0.049174 | 0.069542
Proportion of Photon Fluctuation (√(n)/n)
Photons
Canon A570IS
7.1 Megapixels
1/2.5” sensor
5.76 x 4.29mm (24.7mm2)
Density: 3.48 μm2/pixel

## Slide 8
ISO100
ISO200
ISO400
ISO800
ISO1600
Canon A570IS
7.1 Megapixels
1/2.5” sensor
5.74 x 4.3mm (24.7mm2)
Density: 3.48 μm2/pixel
Chart: 
| 3308.4507042253372 | 1654.2253521126686 | 827.11267605633429 | 413.55633802816703 | 206.77816901408357
Canon A570IS | 0.017386 | 0.024587 | 0.034771 | 0.049174 | 0.069542
100
200
400
800
1600
images: dcresource.com

## Slide 9
Chart: 
| 6915.0521609537618 | 3457.5260804768795 | 1728.7630402384395 | 864.38152011921989 | 432.19076005961
 | 0.012025 | 0.017007 | 0.024051 | 0.034013 | 0.048102
ISO100
ISO200
ISO400
ISO800
ISO1600
Fuji F30
6.1 Megapixels
1/1.7” sensor
7.7 x 5.77mm (44.4mm2)
Density: 7.27 μm2/pixel
100
200
400
800
1600
images: dcresource.com

## Slide 10
Chart: 
| 49258.247193163508 | 24629.123596581754 | 12314.561798290879 | 6157.2808991454394 | 3078.6404495727197
 | 0.0045057 | 0.006372 | 0.0090114 | 0.012744 | 0.018023
ISO100
ISO200
ISO400
ISO800
ISO1600
Canon 30D
8.2 Megapixels
APS-C sensor
22.5 x 15mm (337.5mm2)
Density: 41.16 μm2/pixel
100
200
400
800
1600
images: dcresource.com

## Slide 11
30D
30D
F30
F30
A570IS
A570IS
8.2 Megapixels
22.5 x 15mm (337.5mm2)
Density: 41.16 μm2/pixel
6.1 Megapixels
7.7 x 5.77mm (44.4mm2)
Density: 7.27 μm2/pixel
7.1 Megapixels
5.76 x 4.29mm (24.7mm2)
Density: 3.48 μm2/pixel

## Slide 12
Chart: 
| ISO100 | ISO200 | ISO400 | ISO800 | ISO1600
Canon A570IS | 0.017386 | 0.024587 | 0.034771 | 0.049174 | 0.069542
Fuji F30 | 0.012025 | 0.017007 | 0.024051 | 0.034013 | 0.048102
Canon 30D | 0.0045057 | 0.006372 | 0.0090114 | 0.012744 | 0.018023
Canon 5D | 0.0035355 | 0.005 | 0.0070711 | 0.01 | 0.014142
Proportion of Photon Fluctuation (√(n)/n)
ISO

## Slide 14
Making matters worse, circuitry must occupy some space between each photowell – the more photowells, the more space circuitry takes up.

## Slide 15
Summary
More pixels, smaller sensor => less light per pixel => more noise
Less pixels, bigger sensor => more light per pixels => less noise
In theory, the biggest sensor with the least pixels will give us the best image, in terms of noise.
A 1-pixel sensor would be ideal.
With 1 pixel, we’d have low noise but no detail.
Many pixels => High detail, high noise
Few pixels => Low detail, low noise
The “Megapixel Myth”: Detail vs. Noise

## Slide 16
Megapixels: Detail vs. Noise
Facebook profile picture:
4x6 studio print at 300dpi:
5x7 studio print at 300dpi
Standard VGA TV:
1080p HDTV:
1280x1024 19” LCD monitor:
8.5x11in, 300dpi magazine spread:
8x10 inkjetprint at 200dpi:
10x14in, 150dpi full-page spread in Daily Cal:
Giant 20x30in poster print at 150dpi:
0.03 MP
2.16 MP
3.15 MP
0.35 MP
2.07 MP
1.31 MP
8.42 MP
3.20 MP
3.15 MP
13.5 MP
How many pixels do we need?:
If you only look at pictures on the computer, 2-3MP
If you make non-poster-size prints (4x6, 5x7, 8x10), 3-4MP
More pixels beyond this don’t add detail, and contribute to greater noise